## Slide 1: Basic Electronics and Electrical Engineering
By- chandana mn (cse-087)
Harshitha masur(AE-016)
Priyanka hansda(AE-009)
Assigned by- DR.harinath aireddy

## Slide 2: MAXIMUM POWER TRANSFER THEOREM

## Slide 3: Aim
To verify maximum power transfer theorem for the given circuit.
OR
To prove Maximum Power Transfer theorem practically.

## Slide 5: According to the theorem
RL = R th ……. For maximum power transfer.
IL = Vth / (R th + RL)
= Vth / (R th + R th)
= Vth / 2 R th
where, Pmax =IL2 RL= Vth2 / 4Rth
A graph of RL against P is shown in Fig.(1), the maximum value of power which occurs when RL = R th

## Slide 6
Click to add text

## Slide 7: Apparatus required
Sl.No | Apparatus | Range | Quantity
1 | RPS | (0-30V) | 1
2 | Resistor | 1KΩ or 470Ω or 1.5KΩ | 1
3 | DRB | - | 1
4 | Bread Board & wires | - | -
5 | Ammeter | (0-20mA) | 1

## Slide 8: Circuit diagram

## Slide 9: Observation table
Sl.No | RL in Ω | IL in mA | Power Pmax = IL 2 .RL in mW
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
6 |  |  | 
7 |  |  | 

## Slide 10: Model graph

## Slide 11: Procedure
1. Connect the circuit shown in diagram.
2. Switch ON the DC power supply.
3. Set the input DC voltage to the constant value i.e. either 5V or 10V.
4. Set the DRB or load resistance RL value in steps of 100Ω or 200Ω depend upon the Rth value.
Note down the current in ammeter.
5. Repeat the same for 8 to 9 steps.
6. Calculate the value of Power.
7. Plot the power v/s load resistance graph.

## Slide 12: Result
Thus maximum power theorem was verified when Rth= RL both practically and theoretically.